SECTION 07 62 00

SHEET METAL FLASHING AND TRIM

The information highlighted in yellow below is for insertion into

Section 076200, Sheet Metal Flashing and Trim

Display hidden notes to specifier in Word 2003 by using "Tools"/"Options"/"View"/"Hidden Text".

Display hidden notes to specifier in Word 2007 or later by clicking on the Show/Hide icon (¶)

This section is based on the products of RoofScreen Mfg., Inc., which is located at:

347 Coral St.

Santa Cruz, CA  95060

Toll Free Tel: 866-766-3727

Tel: 831-421-9230

Fax: 866-253-0738

Email: info@roofscreen.com

Web: www.roofscreen.com

RoofScreen Mfg. Inc. designs, manufactures and distributes rooftop equipment screens and supports, watertight roof attachment hardware, acoustical panel systems and architectural aluminum louvers.

This specification is for our DryCap rooftop equipment sleeper cap system, including end caps and cleats for support. For information and specifications for our other products, please see www.roofscreen.com.

For insertion into Section 076200, Aluminum Sheet Metal Flashing and Trim.  Copyright 2016, All Rights Reserved. 160412

GENERAL

  - SUMMARY

    - Aluminum sheet metal flashing, panels, sleeper caps, and trim as shown on the Drawings and specified herein.

      - Extruded cap system for [wood sleepers][form steel curb rails].

PRODUCTS

  - MATERIALS

    - Aluminum Sleeper Caps:  0.100 inch thick, extruded aluminum, ASTM B 209, Alloy 6063-T6.

      - Acceptable Manufacturer:

        - RoofScreen Mfg., which is located at: 347 Coral St.; Santa Cruz, CA 95060; Toll Free Tel: 866-766-3727; Tel: 831-421-9230; Fax: 866-253-0738; Email: request info (info@roofscreen.com); Web: www.roofscreen.com.

        - Substitutions:  Not permitted.

        - Requests for substitutions will be considered in accordance with provisions of Section [012500, Substitutions Procedures][016000, Product Requirements and Substitutions].

      - Aluminum Sleeper End Caps:  0.100 inch aluminum sheet.

** NOTE TO SPECIFIER ** Select steel cleats if there are uplift loads to be resisted and aluminum cleats if only dead loads are on cap.

      - Cleats for Extruded Sleeper Cap System:  1/4 inch thick [hot-dipped galvanized steel, ASTM A 36][aluminum, ASTM B 209, Alloy 6063-T6].

      - Finishes:  Manufacturer’s standard finishes.

    - Fasteners for Aluminum Sleeper Caps:

      - Cleats to Wood:  Simpson SDS Wood Screws.

      - Cleats to Steel:  #12 T3 SDS.

      - Cap to Cleats:  1/4 inch x 1/2 inch stainless-steel thread-cutting screws.

EXECUTION

  - INSTALLATION

    - Install sleeper caps in accordance with manufacturer’s written instructions.

END OF SECTION